## Slide 1: TV Terminology 101: Part 1
Eric Moore
Computer Users Group of Greeley

## Slide 2: Flat-panel Technology
Plasma
  Each pixel consists of three gas-filled cells
  Electric current ionizes the gas, emitting UV that stimulates the cells’ phosphors
  Unlimited viewing angle
  Excellent color and contrast
  Glossy finish is not as good for bright rooms
  Found mainly in display sizes exceeding 43”
LCD (Liquid Crystal Display)
  Electric current causes crystals to polarize, blocking the backlight
  Unblocked pixels allow light to pass through
  Lower energy consumption than plasma
  Limited viewing angle
  Less fluid motion (suffers from “motion blur”)
  Matte finish is better for bright rooms
  Wide selection of display sizes

## Slide 3: Backlight Technology
Fluorescent
  Uses fluorescent light source
  Lower color and contrast quality than LED
LED (Light-Emitting Diode)
  Electrical component called a “diode” generates light for every pixel
  Lower energy use than fluorescent backlight
  Used in newer LCD TVs
  “Local dimming” provides better contrast and more fluid motion

## Slide 4: OLED Displays
Organic LED is used in small electronics and some newer LCD TVs
Thin-film transistor layer contains circuitry for every pixel
Thinner display—no separate backlight required
More energy efficient than plasma or LCD
Excellent color and contrast
Unlimited viewing angle
Fluid motion
New kid on the block: 55” displays currently run between $9,000 and $10,000

## Slide 5: Specifications
Aspect ratio: display size—expressed as a ratio of the number of pixels horizontally vs. vertically
Color resolution: the number of distinct colors than may be represented
Contrast ratio: the difference between the darkest blacks and brightest whites
Frame rate: the number of still frames that may be displayed per second (measured as fps)
Light output: the amount of light produced by the display as measured in lumens
Viewing angle: the maximum angle from which the display may be watched without loss of detail

## Slide 6: Scanning Specifications
Interlaced scan: the “lines” in the display are “drawn” in two sweeps—first the odd-numbered, then the even-numbered
  Indicated by “i” after the vertical measurement (e.g. 1080i)
Progressive scan: the “lines” in the display are “drawn” all in one sweep; doubles the frame rate of interlaced scan
  Indicated by “p” after the vertical measurement (e.g. 1080p)

## Slide 7: High Definition TV
High definition (HDTV): specifies a display size of:
  1920x1080p
  1920x1080i
  1440x1080i
  1280x720p
Ultra-high definition (UHD): specifies a display size of:
  2160p (4K UHD)
  4320p (8K UHD)

## Slide 8: Resolution Adjustment
Downconversion: process by which a TV scales down the picture resolution
  Example: reducing 1080 down to 720
  Picture detail is lost
Upconversion: process by which the picture is scaled up to a higher resolution
  Example: increasing 720 to 1080
  Can result in some “pixelation” of the image

## Slide 9: Other TV Technologies
Smart TV: TV that is linked to a local network or network
  Networking may be built into the set or achieved with a separate set-top box
  Supports streaming content such as Netflix, accessing on-screen programming guides, and user interaction
3D TV: TV that creates the illusion of depth and distance
  Some require special glasses (active shutter 3D or polarized 3D)
  Some are autostereoscopic (no glasses required)

## Slide 10: Questions?